X3-EPS Parallel Box Product Introduction
product department：Yanni
www.solaxpower.com

---
What is X3-EPS Parallel Box?
’？
1
3
4

---
Which products can be used?
X3-Hybrid/Fit
Can multi - generation, multi - power section, multi - machine combination.
1
3
4

---
Contents
Introdution
Product appearance
Installation Operation
Screen Setting Master
Logout
Fault Error
Product Model
Work Mode
Dip Switch
LCD Display Information
Function Introduction
1
3
4

---
Introdution
Standard Operating temperature（℃）: -5~+40
Degree of protecion: IP65
Installation: wall-mounted
Open cover : needed， salt mist35±2℃，24H*7
Connection direction: down-in, down-out
Communication interface: I/O
Safety : IEC62109、IEC61477、IEC61439.

---
Product Model

---
Product appearance
尺寸
端子

---
Work Mode

---
Installation Operation
First step: Connection  wiring
Second step：Dip switch
Third step: Screen setting master

---
Installation Operation

---
Installation Operation -connection  wiring
Please note the inverter connected with be the Master Inverter and this Master inverter must be connected with battery.

---
Dip Switch

---
Screen Setting Master

---
LCD Display Information

---
Logout

---
Function Introduction

---
Function Introduction

---
Function Introduction
The system tends to allocate the power demand of the system to each subsystem according to the ratio of the power type of the coefficient. For example: 12KW power demand, if the system has three A/B/C inverters, their power types are respectively 5KW/8KW/10KW. The A inverter will be allocated (5/23) *12KW power demand, the B inverter will be allocated (8/23) *12KW power demand, and the C inverter will be allocated (10/23) *12KW power demand. When there is no
grid ,EPS on the load is also such a way of working.

---
Fault Error
When more than one inverter is set as the master, the master will report a "parallel Fault" ;
When master and slave software versions are inconsistent, the slave will report a "parallel Fault" ;
When normal communication, the slave has multiple packet loss, the slave will report a "parallel Fault" ;

---
Thank you!